## Slide 1
Semantic Knowledge Base Search
From keyword matching to meaning-based retrieval

## Slide 2
Before: Keyword Search Had Three Hard Limits
Synonym blind
  • searching “escape” misses clauses written as “evacuation”
No cross-lingual
  • querying “exit” never matches the Chinese “出口”
No natural language
  • you can only type keywords, not ask a real question

## Slide 3
This Week ① — Semantic Search Launched
Every code clause → a 1024-dim vector;
then a question finds the semantically nearest clause — meaning, not wording.
 | Choice | Why
Model | bge-m3 | free, multilingual, zh–en aligned
Runtime | ONNX CPU | runs on any laptop, no GPU
Corpus | 1,590 chunks | from existed knowledge base
results
Capability | Question | Hit
Synonym | “escape stair width” | CN evacuation stairs + SG “1.5m in width”
Cross-lingual | “how wide should escape stairs be” | SG Fire Code clause
Natural language | “Can gas pipes run in a residential stairwell?” | CN gas-pipe clause
Concrete scene | “Exits needed for an underground car park?” | CN car park + exit clauses
Indirect / alias | “room at a corridor dead-end” | CN dead-end-room clause

## Slide 4
This Week ② — How Well Does It Work? (Measured honestly)
How we tested: 63 questions — 55 that the knowledge base should answer, plus 8 on topics it does NOT cover (to verify it won't fabricate answers).
Metric | What it means | Result (55 questions)
P1 | The very first result is the correct clause | 67%
P3 | The correct clause appears somewhere in the first 3 results | 84%
Recall | Share of the clauses that should be found that actually were | 84%
F1 | One combined score of accuracy and completeness | 75%
Document-level (looser test) | Only the right document was found — the exact clause may be wrong | 91%
Finding the document ≠ finding the clause
  • 91% only means the right code book was found (e.g. GB 55037); 67% means the exact sentence. 67% is the honest number.
Not a replacement for keyword search
  • A standard keyword method (BM25) scored 71%, close to ours. Semantic search wins on synonyms, cross-language and natural wording — so we keep both.
Anti-fabrication guard
  • On the 8 questions outside the knowledge base, confident-but-wrong answers fell from 8/8 to 4/8, and no correct answer was ever blocked (0/55).

## Slide 5
The Road to Production-Ready Compliance Checking
A 6-tier industry-standard roadmap · progress & next steps

## Slide 6
The Roadmap at a Glance — 6 Tiers
Tier | Done (this week) | Plan (next) | Progress
1 · IFC reading | spaces · doors · structure · MEP · electrical read; exact area / volume / material; mixed-unit fix | connections · distribution systems · openings · quantity sets · profile shapes | ~70%
2 · Quality validation | QA 4 checks (units / spaces / geometry / boundaries); honest “not checked / area unknown” | IDS parser + semantic validation (missing attributes, wrong classification) | ~40%
3 · Geometry & quantities | exact area (triangle projection) · exact volume · material take-off · basic clash pre-check | boolean operations (CSG kernel) · swept solids · exact sections | ~85%
4 · Clash & coordination | MEP vs structure bbox + point-in-mesh confirmation (real vs bbox noise) | full-discipline clash · clear-height checks · grading (hard / soft / clearance) | early
5 · Rules | 5 disciplines · 16 rules (CN + SG) · clause → rule tool | 16 → 50+ (fire / egress / MEP) · context & exceptions · cross-rule linkage | ~15%
6 · Delivery & trust | BCF 2.1 · COBie CSV · HTML/Excel/PNG · 4 samples run | BCF viewpoints · fuller COBie · IFC with annotations · 10+ real projects · benchmark | ~35%
Foundation built: precise geometry + real samples + multi-discipline rules + delivery formats

## Slide 7
This Week's Breakthrough — Precise Geometry & Quantities (Tier ③)
Exact area
  • triangle projection replaces convex hull — previouslyL-shaped room 36 → 27 m², now no over-estimate
Exact volume
  • signed-tetrahedron — office_3f slab 96.9 m³ / Schependomlaan structural total 287.4 m³
Material & quantity take-off
  • per-material volume + per-type counts → “structural quantities by material”
Mixed-unit repair
  • models declared in mm but modelled in metres auto-corrected (Schependomlaan)
Basic clash pre-check
  • MEP vs structure bbox + point-in-mesh confirmation — real penetration, not bbox noise

## Slide 8
Next Steps — Consolidated
Knowledge-base search
1. Attack hard queries
  • query rewriting / domain aliases — hard-query hit rate is now 45%
2. Cross-code retrieval
  • route by CN / SG, or split the query — cross-code recovery is 33%
3. Stronger guard
  • top1−top2 score margin — no false rejects so far (0/55)
4. Grow the gold standard
  • keep adding test queries as the knowledge base grows
Platform — 6-tier roadmap
1. Rule expansion
  • 16 → 50+ rules, fire / egress / MEP first (2–3 wks)
2. IDS quality checking
  • subset parser + semantic validation (1–2 wks)
3. Clash deepening
  • full-discipline clash + clear-height + grading (2 wks)
4. Delivery
  • BCF viewpoints · fuller COBie · 10+ real projects (1–2 wks)