## Slide 1
The Road to Production-Ready Compliance Checking
A 6-tier industry-standard roadmap · progress & next steps
ArchCheck · 2026-08-25

## Slide 2
The Roadmap at a Glance — 6 Tiers
Tier | Done (this week) | Plan (next) | Progress
1 · IFC reading | spaces · doors · structure · MEP · electrical read; exact area / volume / material; mixed-unit fix | connections · distribution systems · openings · quantity sets · profile shapes | ~70%
2 · Quality validation | QA 4 checks (units / spaces / geometry / boundaries); honest “not checked / area unknown” | IDS parser + semantic validation (missing attributes, wrong classification) | ~40%
3 · Geometry & quantities | exact area (triangle projection) · exact volume · material take-off · basic clash pre-check | boolean operations (CSG kernel) · swept solids · exact sections | ~85%
4 · Clash & coordination | MEP vs structure bbox + point-in-mesh confirmation (real vs bbox noise) | full-discipline clash · clear-height checks · grading (hard / soft / clearance) | early
5 · Rules | 5 disciplines · 16 rules (CN + SG) · clause → rule tool | 16 → 50+ (fire / egress / MEP) · context & exceptions · cross-rule linkage | ~15%
6 · Delivery & trust | BCF 2.1 · COBie CSV · HTML/Excel/PNG · 4 samples run | BCF viewpoints · fuller COBie · IFC with annotations · 10+ real projects · benchmark | ~35%
Foundation built: precise geometry + real samples + multi-discipline rules + delivery formats — now we build up.

## Slide 3
This Week's Breakthrough — Precise Geometry & Quantities (Tier ③)
Exact area
  • triangle projection replaces convex hull — L-shaped room 36 → 27 m², no over-estimate
Exact volume
  • signed-tetrahedron — office_3f slab 96.9 m³ · Schependomlaan structural total 287.4 m³
Material & quantity take-off
  • per-material volume + per-type counts → “structural quantities by material”
Mixed-unit repair
  • models declared in mm but modelled in metres auto-corrected (Schependomlaan)
Basic clash pre-check
  • MEP vs structure bbox + point-in-mesh confirmation — real penetration, not bbox noise
Unlocks what's downstream: quantities, clash detection, clear-height checks — all depend on real geometry.

## Slide 4
Where We Stand — Done vs Still Open (honest)
Already in place
• 5-discipline rule engine (CN + SG)
• BCF 2.1 / COBie export
• Clause → machine-rule tooling
• Semantic knowledge-base search
• Precise geometry, volumes, materials
• Real samples: Duplex_MEP, Schependomlaan
Still open (flagged, not hidden)
• Boolean operations (openings) — needs CSG kernel
• IDS-based quality validation
• Rule volume: 16 → hundreds
• Full-discipline clash + clear-height checks
• BCF viewpoints · full COBie
• Scale benchmark vs commercial tools
Everything we can't do yet is stated explicitly — no silent omissions.

## Slide 5
Next Steps — Prioritised
Priority | Action | Effort
1 | Rule expansion: 16 → 50+, fire / egress / MEP first | 2–3 wks
2 | IDS quality checking (subset parser) | 1–2 wks
3 | Clash deepening: full-discipline + clear-height + grading | 2 wks
4 | Delivery: BCF viewpoints · fuller COBie · 10+ real projects | 1–2 wks
Long-term hard items
• Boolean operations (CSG kernel) · full rule coverage · benchmark vs commercial tools
Foundation is built — next is rule volume, IDS validation, and clash depth.